## Slide 1
2025 Offseason Mechanical Seminar
Authored By: John Thibert
Latest Revision: 05/20/2025
Seminar 1 – Engines and Motors

## Slide 2
Revision Table | 
Date (MM/DD/YYYY) | Description
05/20/2025 | Release

## Slide 3: Engines vs Motors
Engines convert CHEMICAL energy into mechanical energy
Motors convert ELECTRICAL energy into mechanical energy

## Slide 4: Engine Types
Typically named after their thermodynamic cycle
Different use cases, efficiencies, and practicalities
Some can even be a hybrid of two different cycles
Well focus on one: Otto cycle

## Slide 5: The Otto Cycle
Typically cover all gasoline car engines
4 stroke & 2 stroke engines
Typical efficiencies are in the realm of 30-40% efficient
​
Isentropic: A process where no heat is added or lost and everything happens in a perfectly efficient way, like an ideal, lossless compression or expansion of gas.
Isochoric: A process where the volume stays the same, so the gas is heated or cooled without changing its size.
η = thermal efficiency (ideal)
r= compression ratio (typically between 8:1 and 12:1 for modern gasoline engines)
𝛾 = specific heat ratio (typically ~1.4 for air)
Theoretical max

## Slide 6: Deeper Dive into 4 Stroke Car Engines
Engines have 6 main systems:
  Cooling system
    Radiator, heater, fans, etc
  Fueling system
    Fuel pump, injectors, etc
  Ignition system
    Ignition coils, spark plugs, etc
  Lubrication system
    Oil pump, bearings, etc
  Intake/Exhaust system
    Turbochargers, superchargers, manifolds, etc
  Mechanical system
    Pistons, connecting rods, valves, camshafts, actuators

## Slide 7: Engine Timing
Involves both ignition timing, and valvetrain timing
Camshafts spin at half the crankshaft speed
Extremely important, especially in modern engines where clearances are small

## Slide 8: Engine Cutaway

## Slide 9: Electric Motor Types
All electric motors operate in one main way:
  Use electricity to generate magnetic fields
  Magnetic fields create forces that cause motion
However, the ways that motors accomplish this vary greatly
Three main architectures:
  Stepper
  Brushed
    Brushed DC motors – The CIM, miniCIM, 775, fall under this category
  Brushless
    Permanent Magnet Synchronous (PMSM) – The NEO, falcon, kraken, fall under this category
    Induction Asynchronous (AM)
    Switched Reluctance (SRM)
    Hybrids exist between these types

## Slide 10: Stepper Motors
These motors step incrementally by a certain number of degrees (a common amount is 1.8°)
Extremely high holding torque
Good for holding positions and moving set amounts without the use of encoders
Require special stepper drivers
Typically draw a lot of power
Typically, low speed, high precision

## Slide 11: Brushed Motors
Easy to drive (just connect power)
Simple operating principle
Lower starting torque than brushless
Typically lower power density than brushless motors
Brushes can wear out over time
No sensors or other electronics required to drive
FRC example: CIM, miniCIM, 775 Pro

## Slide 12: Brushless Motors
Typically, higher torque, power, and more efficient than brushed motors
High power density
No brushes to wear out
More difficult to drive (need a motor controller)
Typically require internal sensors to run (hall effect)
Offer more precise control (RPM, current control)
FRC Examples: NEO, Kraken, Falcon, NEO Vortex
Rotor
Stator

## Slide 13: NEO Motor Curve

## Slide 14
Questions & Open Discussion